## Slide 1
CS-221 PROJECT PRESENTATION
Smart Corridor Ventilation & Air Quality Monitoring System
A RISC-V based embedded system integrating IoT sensors, low-level architecture, and 3D visualization for autonomous indoor air quality control.
CS-221 | Computer Organization & Assembly Language | BSCS-3B | Group 05

## Slide 2
Meets the Team
FA
Faizan Anwar
455259
Team Rep • System Architect & Lead Developer
AM
Abdul Moiz
465932
Hardware Simulation Specialist
MT
Muhammad Taha
467244
Software Engineer (Assembly)
S
Sham
457919
Testing & Validation Engineer

## Slide 3
Problem Statement
The Challenge
Conventional ventilation systems are manual or timer-based, failing to respond dynamically to real-time hazards choices.
Hypercapnia Risk: Elevated CO2 levels (>1000 ppm) cause fatigue
Particulate Accumulation: PM2.5 particles (>100 µg/m³) damage health
Fire Hazards: Smoke infiltration requires immediate mitigation
Delayed Response: Manual systems have dangerous reaction latency

## Slide 4
Project Objectives
⚡
Real-Time Response
Detect hazards within milliseconds using RISC-V
🤖
Autonomous Control
Activate ventilation without human intervention
📊
Multi-Sensor Fusion
Combine Smoke, PM2.5, CO2, and Temperature
🏠
Digital Twin
Immersive 3D simulation for monitoring

## Slide 5
System Architecture: Three-Layer Design
Layer 1: Ripes
RISC-V Architecture
Low-level processor simulation with Memory-Mapped I/O and register manipulation.
Layer 2: Wokwi
IoT Hardware Layer
ESP32-based sensor node with real sensors, WiFi, and MQTT communication.
Layer 3: Simulation
3D Digital Twin
React + Three.js immersive environment with particles and physics.

## Slide 6
Architecture Block Diagram
RISC-V Core
Registers x0-x31 | ALU
System Bus (Data / Address / Control)
0xF0000000
Smoke + PM2.5
0xF0000004
CO2 Level
0xF0000008
LED Matrix
Smoke Detector
PM2.5 Sensor
CO2 Sensor
Fan + LEDs

## Slide 7
Layer 1: Ripes (RISC-V Simulation)
What is Ripes?
Visual RISC-V Processor Simulator
Pipeline visualization (IF, ID, EX, MEM, WB)
Register file inspection
Memory-Mapped I/O support
Why RISC-V?
Open-source ISA (no licensing)
Reduced instruction set = efficiency
Deterministic timing for safety
Educational transparency

## Slide 8
Memory-Mapped I/O Configuration
Address Name Bit Layout Purpose
0xF0000000 Switch Bank 0 Bit 0: Smoke | 1-7: PM2.5 Read Sensor States
0xF0000004 Switch Bank 1 Bits 0-7: CO2 Level Read CO2 Sensor
0xF0000008 LED Matrix 35x25 Pixel Grid (875 px) Visual Feedback
LED Status Codes:
GREEN = Safe
RED = Danger
BLUE = Fan Active

## Slide 9
RISC-V Assembly: Core Logic
# Sensor Polling & Smoke Check (Critical Priority) main_loop: li t0, 0xF0000000 # Load Switch Bank 0 Address lw s0, 0(t0) # Read Raw Input (Smoke + PM2.5) li t1, 1 # Mask for Bit 0 and a0, s0, t1 # Isolate Smoke Bit bnez a0, unsafe_mode # BRANCH IMMEDIATE if Smoke! # PM2.5 Parsing srli a1, s0, 1 # Shift right (remove Smoke bit) li t1, 0x7F # Mask 0111 1111 (7-bit PM2.5) and a1, a1, t1 # Clean PM2.5 value li t2, 100 # Threshold constant bgt a1, t2, unsafe_mode

## Slide 10
Layer 2: Wokwi (IoT Hardware Simulation)
Hardware Components
ESP32 Microcontroller (WiFi)
Potentiometers (Analog Sensors)
Slide Switch (Digital Smoke)
RGB LEDs (Status)
Connectivity
WiFi: Wokwi-GUEST
MQTT: broker.hivemq.com
Topic: smart-corridor/sensors
Topic: smart-corridor/commands

## Slide 11
RISC-V Style Decision Logic (C++)
// Priority-based hazard detection if (effective_smoke > 30) { status_msg = "CRITICAL: SMOKE DETECTED"; alert_level = "critical"; // Priority 1 } else if (effective_temp > 35) { status_msg = "DANGER: HIGH TEMPERATURE"; alert_level = "danger"; // Priority 2 } else if (effective_pm25 > 80) { status_msg = "WARNING: HIGH PM2.5"; alert_level = "warning"; // Priority 3 }

## Slide 12
Layer 3: 3D Digital Twin Simulation
Technology Stack
React (Component UI)
Three.js / Fiber (3D Rendering)
Rapier (Physics Engine)
Vite (Build Tool)
Environment Features
First-Person Controller
Dynamic Smoke Particles
Interactive Appliances
Real-time Alert Lighting

## Slide 13
Simulation Capabilities
🌫️ Fog System
Thousands of particles visualizing smoke spread
📊 Dashboard
Live overlay showing CO2, PM2.5, AQI
💨 Ventilation
Fans spin and clear smoke on command
🚨 Alert Lights
House lights change color (Green -> Red)

## Slide 14
System Integration via MQTT
3D Simulation
(React)
[Publishes Sensors]
MQTT Broker
hivemq.com
<Topics>
/sensors
/commands
Wokwi (ESP32)
(RISC-V Logic)
[Publishes Commands]

## Slide 15
Implementation Flow
1. Requirement Analysis: Define thresholds & safety standards
2. RISC-V Logic Design: Assembly code in Ripes
3. IoT Layer Development: ESP32 firmware in Wokwi
4. 3D Environment: React Three Fiber house model
5. Integration: MQTT bridge connection
6. Testing: Validation of all fail-safes

## Slide 16
Testing & Validation Strategy
Unit Testing
Masking Logic (AND ops)
Branch Logic (Thresholds)
LED Drawing (Mem Addresses)
Integration Testing
Smoke Switch Latency (<1 cycle)
Noisy Data Rejection
MQTT Round-Trip (<500ms)

## Slide 17
Live Demo Phase
Demonstrating the full loop:
1. Ripes: Real-time Register Switching 2. Wokwi: Sensor & Actuator Hardware 3. 3D Sim: Visual Environmental Response

## Slide 18
Conclusion & Future Work
Key Achievements
Full RISC-V implementation
IoT + Digital Twin integration
<100ms Safety Response
Future Enhancements
FPGA Hardware Implementation
Machine Learning Prediction
Mobile App Monitoring
Thank You! Questions?